## Slide 1: Topic 2: Gates, Gate-Based Circuits, and Simulating Circuits
CIS 240: MICROCOMPUTER ARCHITECTURE & PROGRAMMING
1/27/2025 – 1/29/2025
Do before class: Last week’s homework

## Slide 2: Quiz
Fill in table: (Use 8-bits to express numbers)
Base-10 | Positive binary
33 | 
 | 00001101
100,000 | 
-14 | 

## Slide 3: Quiz
Fill in table: (Use 8-bits to express numbers)
What is -5 is ASCII?
What is the following half precision floating point number in base-10 [ Bits: S(1), Exp(5), Significand(10) ]
1100001000000000
Base-10 | Positive binary | 2’s complement
-14 |  | 
 | 00001101 | 
 |  | 11101101

## Slide 4: Cal Poly

## Slide 5: This week…
Logic gates
Building circuits from gates
Circuit simulator

## Slide 6: Logic Gates
Things to know about every basic gate
  Gate name
  Truth Table
  Symbol
  Notation (how it looks in an equation)
  If you’re interested: (Not a requirement for course)
    Ask me if you are interested in more hardware information.

## Slide 7: Symbol (AND) and notation
AND Gate
Notation
  A•B=OUT
A
B
OUT
Input |  | Output
A | B | OUT
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 8: The word “AND” (Gate name)
Is [(6==8) AND (7==9)] true? F or 0
Is [(6==8) AND (7==7)] true? F or 0
Is [(6==6) AND (7==9)] true? F or 0
Is [(6==6) AND (7==7)] true? T or 1
A generic version of the above question:
  Is [A AND B] true?

## Slide 9: The word “AND” (Gate name)
Is [(6==8) AND (7==9)] true? F or LOGIC 0
Is [(6==8) AND (7==7)] true? F or LOGIC 0
Is [(6==6) AND (7==9)] true? F or LOGIC 0
Is [(6==6) AND (7==7)] true? T or LOGIC 1
A generic version of the above question:
  Is [A AND B] true?

## Slide 10: Truth Table (AND)
 | Input |  | Output
Example Sentences: (A AND B) | A | B | TRUE?
Is [(6==8) AND (7==9)] true? | 0 | 0 | 0
Is [(6==8) AND (7==7)] true? | 0 | 1 | 0
Is [(6==6) AND (7==9)] true? | 1 | 0 | 0
Is [(6==6) AND (7==7)] true? | 1 | 1 | 1
Let’s use logic values
  1: TRUE
  0: FALSE
A
B

## Slide 11: Symbol (AND) and notation
AND Gate
Notation
  A•B=OUT
A
B
OUT
Input |  | Output
A | B | OUT
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 12: As mentioned in Topic 1…
The voltage or current that represents a “(logic) 1” and “(logic) 0” are different for different systems.
On Digilent boards, 2.5V, 1.8V, or 1.2V (depending on how you place jumpers) represents a “1” and 0V represents a logic “0”.

## Slide 13: Symbol (3-input AND) and notation
AND Gate
Notation
  A•B•C=OUT
A
B
OUT
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
C

## Slide 14: Question:
What is the symbol and notation of a 7-input AND gate?
How many lines in the truth table of A 7-INPUT and GATE?

## Slide 15: Inverter (NOT gate)
Symbol
Truth Table
Notation
A
OUT
Input | TRUE?
A | OUT
0 | 1
1 | 0

## Slide 16: We’ve seen:
AND (mathematical partner: A x B)
  2-input, 3-input, 7-input….
NOT (Inverter) (mathematical partner: -A)
Next:
  OR (mathematical partner: A + B)
  XOR
  NAND
  NOR
  XNOR
  (Buffer)

## Slide 17: Symbol (OR) and notation
OR Gate
Notation
  A+B=OUT
Input |  | Output
A | B | OUT
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A
B
OUT

## Slide 18: Symbol (OR, 3-input) and notation
OR Gate
Notation
  A+B+C=OUT
A
B
OUT
C
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 19: Symbol (XOR) and notation
XOR Gate (Exclusive OR gate)
Notation
  Meaning:
  True if A ≠ B
Input |  | Output
A | B | OUT
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
OUT

## Slide 20: Multiple input XOR gates
Logic operators are associative in nature
A
B
C
D
E
F
OUT

## Slide 21: Multiple input XOR gates
How many lines in truth table?
Let’s just do some of it…
Do you see a pattern
Input |  |  |  |  |  | Output
A | B | C | D | E | F | OUT
0 | 0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 0 | 0 | 1 | 
0 | 0 | 0 | 0 | 1 | 0 | 
0 | 0 | 0 | 0 | 1 | 1 | 
0 | 0 | 0 | 1 | 0 | 0 | 
0 | 0 | 0 | 1 | 0 | 1 | 
0 | 0 | 0 | 1 | 1 | 0 | 
0 | 0 | 0 | 1 | 1 | 1 | 
0 | 0 | 1 | 0 | 0 | 0 | 
⁞ | ⁞ | ⁞ | ⁞ | ⁞ | ⁞ | ⁞
1 | 1 | 1 | 1 | 1 | 1 | 
A
B
C
D
E
F
OUT

## Slide 22: Symbol (Multi-input XOR)
XOR Gate (Exclusive OR
gate)
Notation
  Meaning
  An odd number of ones
A
B
OUT
C
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 23: Symbol (NAND) and notation
NAND Gate
Notation
Input |  | Output
A | B | OUT
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
OUT

## Slide 24: Symbol (3-input NAND) and notation
NAND Gate
Notation
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
A
B
OUT
C

## Slide 25: Symbol (NOR) and notation
NOR Gate
Notation
Input |  | Output
A | B | OUT
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A
B
OUT

## Slide 26: Symbol (NOR, 3-input) and notation
NOR Gate
Notation
A
B
OUT
C
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 27: Symbol (NXOR) and notation
XOR Gate (Exclusive OR gate)
Notation
  Meaning
  A ≠ B
Input |  | Output
A | B | OUT
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
OUT

## Slide 28: Symbol (Multi-input XNOR)
XOR Gate (Exclusive OR
gate)
Notation
  Meaning
  An odd number of ones
A
B
OUT
C
Input |  |  | Output
A | B | C | OUT
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 29: Summary of gates
OR, AND, XOR
NOR, NAND, XNOR
INV (=NOT)
Know: Symbol, mathematical operator and truth table

## Slide 30: Know:
 | AND | NAND | OR | NOR | XOR | XNOR | NOT
Name | and |  |  |  |  |  | 
Symbol |  |  |  |  |  |  | 
Truth table |  |  |  |  |  |  | 
Notation | A·B=out |  |  |  |  |  | 
A
B
out
AB out
00 0
01 0
10 0
11 1

## Slide 31: Finally we build a circuit

## Slide 32: NAND gate
Change this table to a sentence:
IF A is false AND B is false then Output is True
OR
IF A is false AND B is true then Output is True
OR
IF A is true AND B is false then Output is True
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 33: NAND gate
Change this table to a sentence:
IF A is false AND B is false
OR
IF A is false AND B is true
OR
IF A is true AND B is false
Then output is true
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 34: NAND gate
Change this table to a sentence:
IF (A is false) AND (B is false)
OR
IF (A is false) AND (B is true)
OR
IF (A is true) AND (B is false)
Then output is true
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 35: NAND gate
Change this table to a sentence:
IF A AND B
OR
IF A AND B
OR
IF A AND B
Then output is true
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 36: NAND gate
Change this table to a sentence:
IF A • B
OR
IF A • B
OR
IF A • B
Then output is true
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 37: NAND gate
Change this table to a sentence:
(A • B) + (A • B) + (A • B)
= Output
Look at “1”s in Output column
and make sentence
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Sum of products!!!!

## Slide 38: SOP
Find 1s in output column
Look at the inputs
Find an equation ANDing inputs that equals 1 for only those inputs – this is called a “Minterm”:
  “A product (ANDed) term in which each of the n variables appears once (in either its complemented or uncomplemented form) is called a minterm”.
Find all the 1s (outputs) and do steps 1-3 for each
OR all the minterms

## Slide 39: SOP vs POS
SOP: OUT=(A·B)+(A·C)
POS: OUT=(X+Y)·(X+Z)
Input |  | Output
A | B | TRUE?
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0

## Slide 40: POS
Find 0s in output column
Look at the inputs
Find an equation ORing inputs that equals 0 for only those inputs – this is called a “Maxterm”:
  “A sum term in which each of the n variables appears once (in either its complemented or uncomplemented form) is called a maxterm.”.
Find all the 0s (outputs) and do steps 1-3
AND all the maxterms

## Slide 41: Manipulating and Reducing the Number of Gates

## Slide 42
Boolean laws | Description
Annulment law | A · 0 = 0 A + 1 = 1
Identity law | A · 1 = A A + 0 = A
Idempotent law | A · A = A A + A = A
Complement law | A · AC = 0 A + AC = 1
Commutative Law | A · B = B . A A + B = B + A
Boolean laws | Description
Associative law | A · (B · C) = (A · B) · C A + (B + C) = (A + B) + C
Distributive law | A(B + C) = AB + AC A + (BC) = (A + B)(A + C)
Absorption law | A(A + B) = A A + (A · B) = A
Involution law | (A’)’ = A
De Morgan’s law | (A + B)C = AC · BC (A · B)C = AC + BC
https://byjus.com/maths/boolean-algebra-laws/

## Slide 43: De Morgan’s Laws

## Slide 44: De Morgan’s Laws practice

## Slide 45: De Morgan’s Laws practice

## Slide 46: De Morgan’s Laws practice

## Slide 47: De Morgan’s Laws practice SOP to POS

## Slide 48: De Morgan’s Laws on 2-input XNOR

## Slide 49: De Morgan’s Laws on 3-input XNOR

## Slide 50: In This Section We’ll Do:
Logic Reduction
  K-Map SOP
  K-Map POS (We won’t do in class)
Glitchs (We won’t do in class)
We’ll use a tool called a Karnaugh map (K-map) to reduce the number of gates in a design
K-maps can also be used to predict and remove glitches

## Slide 51: Combinational Logic Example Step 4: SOP K-MAP Design problem: 3-bit input, output is input minus 2
1. Draw grid
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
I n p u t s (X)
Inputs
Outputs (Y)
X0 \ X2, X1 |  |  |  | 
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 52: Combinational Logic Example Step 4: SOP K-MAP Y2 logic Design problem: 3-bit input, output is input minus 2
2. Draw circles (2N x 2M)
Y2:
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
X0 \ X2, X1 | 0, 0 | 0, 1 | 1, 1 | 1, 0
0 |  |  |  | 
1 |  |  |  | 
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 53: Combinational Logic Example Step 4: SOP K-MAP Y2 logic Design problem: 3-bit input, output is input minus 2
3. Find logic (Y2 logic)
Y2:
Inside the circle, two 1s are circled
X2,X1,X0 = 110 and X2,X1,X0 = 111
NOTE: X2=1 for both 1s and X1=1 for both 1s
BUT X0=1 for one 1 and X0=0 for the other 1. So X0’s value
doesn’t matter. The output will be 1 no matter what X0 is.
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
X0 \ X2, X1 | 0, 0 | 0, 1 | 1, 1 | 1, 0
0 | X | 0 | 1 | 0
1 | X | 0 | 1 | 0
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 54: Combinational Logic Example Step 4: SOP K-MAP Y2 logic Design problem: 3-bit input, output is input minus 2
3. Find logic (Y2 logic)
Y2:
NOTE: X2=1 and X1=1 for both 1s
BUT X0=1 for one 1 and X0=0 for the
other 1. So X0’s value doesn’t matter.
The output will be 1 no matter what X0 is.
So logic for that circle is:
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
X0 \ X2, X1 | 0, 0 | 0, 1 | 1, 1 | 1, 0
0 | X | 0 | 1 | 0
1 | X | 0 | 1 | 0
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 55: Combinational Logic Example Step 4: SOP K-MAP Y1 logic Design problem: 3-bit input, output is input minus 2
3. Find logic (Y1 logic)
Y1:
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
X0 \ X2, X1 | 0, 0 | 0, 1 | 1, 1 | 1, 0
0 |  |  |  | 
1 |  |  |  | 
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 56: Combinational Logic Example Step 4: SOP K-MAP Y0 logic Design problem: 3-bit input, output is input minus 2
3. Find logic (Y0 logic)
Y0:
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
X0 \ X2, X1 | 0, 0 | 0, 1 | 1, 1 | 1, 0
0 |  |  |  | 
1 |  |  |  | 
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 57: Practice
Draw the Kmap for this truth table
Find minimum logic
Inputs |  |  |  | Output
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 58: Practice
Draw two Kmap that both work for this truth table
Find minimum logic
Input |  |  | Output
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 59: Practice
Draw the Kmap for this truth table
Find minimum logic
 |  | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1

## Slide 60: Draw the truth table for this logic equation:

## Slide 61: Combining Basic Gates to Build Things that Actually Do Stuff

## Slide 62: In This Section We’ll Do:
Combinational Logic and Design Flow using
  SOP (Sum of Products) from truth table
  POS (Product of Sums) from truth table
We’ll go through design steps for design USING GATES
(No VHDL yet)

## Slide 63: Combinational Logic Design
Steps in Designing a Combinational Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
UNDERSTAND PROBLEM!!!!!!!!!
Step 2:
UNDERSTAND PROBLEM!!!!!!!!!
Step 3:
UNDERSTAND PROBLEM!!!!!!!!!
Step 4:

## Slide 64: Combinational Logic Design
Steps in Designing a Combinational Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Truth Table
Step 3:
Generate Logic Equations
Step 4:
Draw Logic
Step 5:

## Slide 65: Combinational Logic Example - Step 1
Step 1:
  Understand Problem
    A Circuit Which Subtracts 2 From a 3-bit Number
  Example:
    If input is 101 (5), output is 011
  Is Description Complete?
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 66: Combinational Logic Example - Step 1
Step 1:
  Understand Problem
    A Circuit Which Subtracts 2 From a 3-bit Number
  Example:
    If input is 101 (5), output is 011
  Is Description Complete?
    What Happens When the Input is 1?
    Let’s Limit Input to Values Greater than 1
    Do you need to define negative number system?
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 67: Combinational Logic Example - Step 2
Step 2:
  Determine I/O
Circuit-to-be
3
3
X
(X2, X1, X0)
Y (= X – 2)
(Y2, Y1, Y0)
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 68: Combinational Logic Example - Step 3
Step 3:
  Tool #1:
  Truth Table
  (A Circuit Which
  Subtracts 2 From a
  3-bit Number, IP>1)
INPUT |  |  | OUTPUT |  | 
X2 | X1 | X0 | Y2 | Y1 | Y0
0 | 0 | 0 | X | X | X
0 | 0 | 1 | X | X | X
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 1
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 69: Combinational Logic Example - Step 4
Step 4:
  Generate Logic Eq.
    From TT
      SOP
      POS
    K-Map
      SOP
      POS
    Guess? (“By examination”)
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 70: Combinational Logic Example - Step 4: SOP
Step 4:
  From TT
    SOP
      Sum of Products
      Look For ‘1’s
X2 X1X0 Y2 Y1 Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 71: Karnaugh Maps
Given a truth table:
A simple question:
  If changing bit B’s value doesn’t change the output, do you need to pay attention to bit B when determining output logic?
A | B | OUT
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0

## Slide 72: Combinational Logic Example Step 4: SOP K-MAP Design problem: 3-bit input, output is input minus 2
Step 4:
  K-map
  Tool #2
    SOP
      Sum of Products
      Look For ‘1’s
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 73: Combinational Logic Example Step 4: SOP K-MAP
Step 4:
  K-map (SOP)
  Most Convenient to Make Xs in First Column zeros.
  Logic Becomes: Y2 = X2•X1
Y2:
0
1
0
X
1
0
1
0
X
0
10
11
01
00
X2 X1
X0
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 74: Combinational Logic Example Step 4: SOP K-MAP
Step 4:
  K-map (SOP)
  Most Convenient to Make Xs in First Column ones.
  Logic Becomes: Y1 = X1
Y1:
1
0
0
X
1
1
0
0
X
0
10
11
01
00
X2 X1
X0
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 75: Combinational Logic Example Step 4: SOP K-MAP
Step 4:
  K-map (SOP)
  Most Convenient to Make X in First Row a Zero and X in Second Row a One. Logic Becomes: Y0 = X0
Y0:
1
1
1
X
1
0
0
0
X
0
10
11
01
00
X2 X1
X0
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 76: Combinational Logic Example Step 4: POS K-MAP
Step 4:
  K-map (POS)
  Most Convenient to Make Xs in First Column zeros. (This table isn’t a good example of POS).
  Logic Becomes:
Y2:
0
1
0
X
1
0
1
0
X
0
10
11
01
00
X2 X1
X0
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 77: K-maps (Karnaugh maps) practice
Truth table, SOP, POS (look for XOR)
D0 \ D2,D1 | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1

## Slide 78: Practice: KMap, 3,2,1: SOP, 0:POS
INPUTS |  |  | OUTPUTS |  |  | 
A(2) | A(1) | A(0) | X(3) | X(2) | X(1) | X(0)
0 | 0 | 0 | 1 | X | 1 | 1
0 | 0 | 1 | 1 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0 | X
0 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | X | 1 | 1
1 | 0 | 1 | X | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | X | 0 | 0

## Slide 79: XOR KMap
 | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 1
01 | 1 | 0 | 1 | 0
11 | 0 | 1 | 0 | 1
10 | 1 | 0 | 1 | 0
AB
CD

## Slide 80: XOR KMap
 | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 1
01 | 1 | 0 | 1 | 0
11 | 0 | 1 | 0 | 1
10 | 1 | 0 | 1 | 0
AB
CD
A | B | C | D | OP
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
… | … | … | … | …
Entire table:

## Slide 81: XOR KMap
 | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 1
01 | 1 | 0 | 1 | 0
11 | 0 | 1 | 0 | 1
10 | 1 | 0 | 1 | 0
AB
CD
A | B | C | D | OP
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
… | … | … | … | …
Random circle: Here  A, D
Note:
Always check to see if XOR or XNOR
A and D are constant and opposite
Equation:

## Slide 82: XOR KMap
 | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 1
01 | 1 | 0 | 1 | 0
11 | 0 | 1 | 0 | 1
10 | 1 | 0 | 1 | 0
AB
CD
A | B | C | D | OP
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
… | … | … | … | …
Random circle: Here  A, C
Note:
Always check to see if XOR or XNOR
A and C are constant and equal
Equation:

## Slide 83: XOR KMap
 | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 1
01 | 1 | 0 | 1 | 0
11 | 0 | 1 | 0 | 1
10 | 1 | 0 | 1 | 0
AB
CD
A | B | C | D | OP
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
… | … | … | … | …
Random circle: Here  A
Note:
Always check to see if XOR or XNOR
A is constant and zero
Equation:

## Slide 84: Combinational Logic Example - Step 4: POS
Step 4:
  From TT
    POS
      Product of sums
      Look For ‘0’s
X2 X1X0 Y2 Y1Y0
0 0 0 X X X
0 0 1 X X X
0 1 0 0 0 0
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 1 0 1
Notes: What happens if the input is 1? What’s the output? Let’s limit input to numbers greater than 1.

## Slide 85: Practice
Converters
  C to F
  Gray code to Binary
  GPA to ASCII
Functions
  Adder
  Multiplier
Value to action
  Button push  Display
  Switch combination to LEDs

## Slide 86: Build circuit that adjusts amplitude
Digital VGA (variable gain amplifier)
When you rotate your radio, the volume stays constant even the reception levels change
3-bits in that represents the average amplitude of a signal
Output is multiplier (fixed point with 2-bits of fraction) that multiplies signal to average volume of “3.5” to “4”.

## Slide 87: Class problem
Add ‘1’ block
+1