## Slide 1: Sequential Logic Design

## Slide 2: Introduction to Sequential Logic
Sequential Logic: Logic that does things in sequence
Design Problem: A Counter
  Counts up to 3 Then Starts Over at 0
OK… Count up 1.
  Can’t Count up Unless You Know What Present Value… You Need Memory. You Need The Present STATE to Figure out the Next STATE. If it’s 2 now then it’ll be 3 next.
When Do You Count up?  On a Signal: Clock

## Slide 3: Clock Pulse Definition
Period
(= 1/frequency)
Positive Pulse
Positive Edge
=Rising Edge
Negative Edge
=Falling Edge
Negative Pulse
Positive Edge
=Rising Edge
Negative Edge
=Falling Edge
CLK
Clock
edge 1
Clock
edge 2
Clock
edge 4
Clock
edge 5
Clock
edge 3
Duty cycle
=% high of period

## Slide 4: Clock Pulse Definition
tf
=fall time
90%
10%
time
tr
=rise time

## Slide 6: Sequential Logic: Introduction

## Slide 7: Counter comments to here
Remember, we’re building a sequential circuit
Flip-flops hold information about present state  The value in the flip-flops is called “Present state” because it tells you where you are in the sequence
“Next state” logic take the “Present state” and calculates what the NEXT STATE will be when the clock ticks
We’ve seen two of the most important blocks

## Slide 8: Complete sequential circuit
A sequential circuit is made up of three parts:
  Present state (PS) flip-flops
  Next state (NS) logic block
  Output logic block
From here we’ll look at the process used to create a sequential circuit

## Slide 9: Sequential Logic: Design Steps and types of sequential logic

## Slide 10: Sequential Circuit Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transition Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 11: Sequential Circuit Design
Example:
  A 2-Bit Up-Down Counter
  Step 1: Understand Problem
    A Circuit That:
      Counts UP on 1 Input (dir)
      Counts DOWN on 0 Input (dir)
      Starts at 0 After RESET Input
      Start-up Value Not Guaranteed
What’s missing?

## Slide 12: Sequential Circuit Design
Example:
  Step 2: Determine I/O
dir direction
RESET reset
clk
Q1Q0
(Count value)
2

## Slide 13: NOTE: What to draw on an IO block
IO only of complete circuit
  No input counter:
  Second design:
IO Diagram
IO Diagram

## Slide 14: Sequential Circuit Design
Example: (State = output)
  Step 3: Describe Behavior with Timing Diagram
Q1Q0 XX 00 01 10 11 00 01 00 11 10 01
State XX 00 01 10 11 00 01 00 11 10 01
CLK
Q1
Q0
RESET
dir

## Slide 15: Sequential Circuit Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transistion Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 16: Alternate picture of Meally and Moore Machines (Maybe easier to understand)
Models: Input doesn’t go to Output Logic block for Moore
Meally Machine
(Output Depends on Input and Present State)
Output
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops
Moore Machine
(Output Depends Only on Present State)
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops

## Slide 17: Sequential Logic Models
Models: Input doesn’t go to Output Logic block for Moore
Meally Machine
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK
(Output Depends on Input and Present State)
Moore Machine
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK
(Output Depends Only on Present State)

## Slide 18: Sequential Logic Models
Meally Machine
  Possible Gains:
    Less Logic
    Fewer States
    Quicker Results
  Possible Dangers
    Glitching
    Feedthrough Loop
Meally Machine
(Output Depends on Input and Present State)
Output
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops

## Slide 19: Sequential Logic Models
Moore Machine
  Possible Gains:
    Robust
    Synchronized
  Possible Drawbacks
    Larger Area
Moore Machine
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK
(Output Depends Only on Present State)

## Slide 20: Sequential Logic Models
Meally Machine
CLK
Input
Output
(Output Depends on Input and Present State)
Output
Combinational
Logic
Output Logic
Input
CLK
Takes Present State and Produces Next State.
FF Holding
Present State
Combinational
Logic
Flip-flops

## Slide 21: Sequential Logic Models
Moore Machine
CLK
Input
Output / D
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK
(Output Depends Only on Present State)

## Slide 22: Sequential Logic Models
CLK
Input
Output / D
Moore Machine
Meally Machine
CLK
Input
Output / D

## Slide 23: Sequential Logic Models
Q3Q2Q1Q0 0000 0001 0010 0011 0100 0101 0110 01110000 0001 0010 0011…
CLK
Q3
Q2
Q1
Q0
Reset
Meally or Moore?

## Slide 24: Sequential Circuit Design
Example:
  Step 4: Select Model Type. Meally or Moore?
CLK
Q1
Q0
Q1Q0 XX 00 01 10 11 00 01 00 11 10 01
RESET
dir
Moore

## Slide 25: Sequential Circuit Design
Example:
  Step 4: Select Model Type. Meally or Moore?
CLK
Q1
Q0
Q1Q0 XX 00 01 10 11 00 01 00 11 10 01
RESET
dir
Meally

## Slide 26: Sequential Logic Models
CLK
Q3
Q2
Q1
Q0
Q3Q2Q1Q0 0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011…
Meally or Moore?

## Slide 27: Sequential Logic Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transistion Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 28: State Transition Diagrams
Different for Meally & Moore Models
Meally
Moore
State Name
State Value
[Input/Output Value]
Next State
State Name
State Value
[Output Value]
Next State
[Input Value]

## Slide 29: Selecting State Bubble Stuff (1)
State name: Something descriptive of the state’s function. Words are good. For humans.
  ie “Add numbers”
State Value: Each state must have a numerical name. It must be unique (different from all other state values in the machine). For computer.
  ie For a four-state machine: 00, 01, 10, 11.
  ie For a five state machine: 000, 001, 010, 011, 100, 101
  ie For a four state machine: 0000, 1001, 1010, 1011, 1100

## Slide 30: Selecting State Bubble Stuff (2)
Output value: A list of ‘1’s and ‘0’s corresponding to the outputs of the state machine.
  ie [1011] for a state machine with outputs [Enable, Add, Subtract, SaveResult]
Input value: A list of ‘1’s and ‘0’s corresponding to the inputs of the state machine (often come from blocks the FSM controls).
  ie [010] for a state machine with outputs [ResetAll, MultiplyDone, Negative?]

## Slide 31: Selecting State Bubble Stuff (3)
Legend/Key – for input and output
  You can write inputs and outputs as 0s and 1s OR you can write the names of the signals. For example the counter’s outputs were: OP1 and OP0
  The output can be written: 10 or
  Non-negated means ‘1’ and negated means ‘0’
BUT: If you write ‘10’, you need to tell me what that means. You need a legend. Here’s an example (on next slide)

## Slide 32: Sequential Circuit Design
State name: Zero, One
State value: 00, 01
Zero
00
[010]
One
01
[111]
0000
0001
0101
1100
1011
1101
• • •
• • •
Key: Input: Button1, Button2, DoorOpen, KeyTurned
Output: StartCar, TurnOnStartLight, LockDoors

## Slide 33: Sequential Circuit Design
Example:
  Step 5: Draw the State Transition Diagram
Zero
00
[0]
One
01
[1]
Two
11
[2]
Three
10
[3]
0
0
0
0
1
1
1
1
RESET
RESET
RESET
RESET
RESET

## Slide 34: Sequential Circuit Design
Example:
  Step 5: Draw the State Transition Diagram
Zero
00
[00]
One
01
[01]
Two
11
[10]
Three
10
[11]
0
0
0
0
1
1
1
1
RESET
RESET
RESET
RESET
RESET

## Slide 35: Sequential Circuit Design
Example:
  Step 6: Draw the State Transition Table
Output Logic
Present State
Output
2
2
Next
State
Logic
Present State
direction
Next State
RESET
2
2
Output Logic
Next State Logic

## Slide 36: Sequential Circuit Design
Example:
  Step 6: Draw the State Transition Table
Output Logic
Present State
Output
P1 P0 O1 O0
0 0 0 0
0 1 0 1
1 0 1 1
1 1 1 0
Zero
00
[0]
One
01
[1]
Two
11
[2]
Three
10
[3]
0
0
0
0
1
1
1
1
2
2
RESET

## Slide 37: Sequential Circuit Design
Example:
  Step 6: Draw the State Transition Table
rst P1 P0 dir N1 N0
0 0 0 0 1 0
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 1
0 1 0 0 1 1
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 0
1 X X X 0 0
Zero
00
[00]
One
01
[01]
Two
11
[10]
Three
10
[11]
0
0
0
0
1
1
1
1
RESET
Next
State
Logic
Present State
direction (dir)
Next State
RESET (rst)
2
2
NOTE: This truth table won’t be acceptable in this class unless I say so in question

## Slide 38: Sequential Circuit Design
Example:
  Step 7: Derive Logic
    Output
      O1=P1
      O0=P1P0
    Next State
      N1=(P1dir)•rst
      N0=(P1dir)•rst
P1 P0 O1 O0
0 0 0 0
0 1 0 1
1 0 1 1
1 1 1 0
rst P1 P0 dir N1 N0
0 0 0 0 1 0
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 1
0 1 0 0 1 1
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 0
1 X X X 0 0

## Slide 39: Sequential Circuit Design
Example:
  Step 8: Draw Logic
    O1=P1
    O0=P1P0
    N1=P1IN
    N0=P1IN
Moore Machine
FF
O1=P1
O0=P1P0
N1=P1IN
N0=P1IN
Input
Output
CLK
2
2
2
2

## Slide 40: Sequential Logic Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transistion Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 41: State Transition Diagrams
Same Example Except Use Meally Model:
Step 1Thru 2 are the Same
  Step 3: Describe Behavior with Timing Diagram
  Step 4: Meally or Moore?
  Meally
CLK
Q1
Q0
Q1Q0 XX 00 01 10 11 00 01 10 11 00 01
Reset

## Slide 42: State Transition Diagrams
Different for Meally & Moore Models
Meally
Moore
State Name
State Value
[Input/Output Value]
Next State
State Name
State Value
[Output Value]
Next State
[Input Value]

## Slide 43: Sequential Circuit Design Non-Mealy Mealy, No need for Mealy
Example:
  Step 5: Draw the State Transition Diagram
Zero
00
One
01
Two
11
Three
10
0/10
0/01
0/00
0
1
1
1
1
RESET/00
Doesn’t work
RESET
RESET/10
RESET/11
RESET/00
/00
/01
/10
/11
/01
/11

## Slide 44: Sequential Circuit Design
Example:
  Step 5: Draw the State Transition Diagram
Zero
00
One
01
Two
11
Three
10
0/01
0/00
0/11
0
1
1
1
1
RESET/00
RESET
RESET/00
RESET/00
RESET/00
/01
/10
/11
/00
/00
/10

## Slide 45: Sequential Circuit Design
Same Example Except Use Meally Model :
  Step 5: Draw the State Transition Diagram
Zero
00
One
01
Two
11
Three
10
0/01
0/00
0/11
0/10
1/10
1/01
1/00
1/11
RESET/00

## Slide 46: Sequential Circuit Design
Same Example Except Use Meally Model :
  Step 6: Draw the State Transition Table
Next
State
Logic
Present State
direction
Next State
RESET
2
2
Output Logic
Present State
Output
direction
RESET
2
2
Output Logic
Next State Logic

## Slide 47: Sequential Circuit Design
Same Example Except Use Meally Model :
  Step 6: Draw the State Transition Table
Zero
00
One
01
Two
11
Three
10
0/01
0/00
0/11
0/10
1/10
1/01
1/00
1/11
Output Logic
Present State
Output
direction
RESET
2
2
rst P1 P0 dir O1 O0
0 0 0 0 1 1
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 0
0 1 0 0 1 0
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 1
1 X X X 0 0

## Slide 48: Sequential Circuit Design
Same Example Except Use Meally Model :
  Step 6: Draw the State Transition Table
Zero
00
One
01
Two
11
Three
10
0/01
0/00
0/11
0/10
1/10
1/01
1/00
1/11
rst P1 P0 dir N1 N0
0 0 0 0 1 0
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 1
0 1 0 0 1 1
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 0
1 X X X 0 0
Next
State
Logic
Present State
direction
Next State
RESET
2
2

## Slide 49: Sequential Circuit Design
Example:
  Step 7: Derive Logic
    Output
      O1=(P0dir)•rst
      O0=(P1P0)•rst
    Next State
      N1=(P0dir)•rst
      N0=(dirP1)•rst
rst P1 P0 dir O1 O0
0 0 0 0 1 1
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 0
0 1 0 0 1 0
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 1
1 X X X 0 0
rst P1 P0 dir N1 N0
0 0 0 0 1 0
0 0 0 1 0 1
0 0 1 0 0 0
0 0 1 1 1 1
0 1 0 0 1 1
0 1 0 1 0 0
0 1 1 0 0 1
0 1 1 1 1 0
1 X X X 0 0

## Slide 50: Sequential Circuit Design
Example:
  Step 8: Draw Logic
    Output
      O1=(P0dir)•rst
      O0=(P1P0)•rst
    Next State
      N1=(P0dir)•rst
      N0=(dirP1)•rst
Meally Machine
Combinational
Logic
FF Holding
Present State
O1=(P0dir)•rst
O0=(P1P0)•rst
N1=(P0dir)•rst
N0=(dirP1)•rst
Input
Output
CLK

## Slide 51: Class Problem: Digital Debouncer
Push-button switches, toggle switches, and electro-mechanical relays bounce:
Let’s say you know that the maximum time a switch can bounce is 1μs+ (a bit more than 1μs) and your clock is at 3MHz. Build (separately) a Meally and a Moore machine that tells you when you’ve stopped bouncing and have gone from 0 to 1.

## Slide 52: Sequential Logic Design
Steps in Designing a Sequential Circuit
UNDERSTAND PROBLEM!!!!!!!!!
Step 1:
Determine I/O
Step 2:
Decide FSM Type (Meally or Moore)
Step 4:
Draw State Transistion Diagram
Step 5:
Draw Logic
Step 8:
Step 3:
Timing Diagram (To Describe & Understand Behaviour)
Write out State Transition Table
Generate Logic Equations
Step 6:
Step 7:

## Slide 53: Sequential Logic: Examples

## Slide 54: My Specifications (Digital Debouncer)
If 4 clock cycles after I see a ‘1’, I see a ‘1’, again then I will assume that the input has switched from 01 and I should output a 1.
Whenever I am in the “found a 1” state and I see a 0, I will switch to the wait state.

## Slide 55: Determine I/O (Digital Debouncer)
Button
Output
clk
Cleaned
Button
Output

## Slide 56: Timing Diagram (Digital Debouncer)
Moore Machine
Input
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Output
CLK
D Q
CLK
CLK
Input
Output

## Slide 57: State Transition Diagram (Digital Debouncer)
Wait/Low
000
[0]
Sensed 1
001
[0]
Sensed 3
011
[0]
Three
101
[1]
0
X
X
1
0
1
Sensed 2
010
[0]
X
Sensed 4
100
[0]
1
0

## Slide 58: Output Logic (Digital Debouncer)
Output Logic
Present State
Output
P2 P1 P0 Out
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 0 1 1
1 1 0 X
1 1 1 X
Out=P2•P1•P0
3

## Slide 59: Next State Logic (Digital Debouncer)
In P2 P1 P0 NS2 NS1 NS0
0 0 0 0 0 0 0
0 0 0 1 0 1 0
0 0 1 0 0 1 1
0 0 1 1 1 0 0
0 1 0 0 1 0 1
0 1 0 1 0 0 0
0 1 1 0 X X X
0 1 1 1 X X X
1 0 0 0 0 0 1
1 0 0 1 0 1 0
1 0 1 0 0 1 1
1 0 1 1 1 0 0
1 1 0 0 1 0 1
1 1 0 1 1 0 1
1 1 1 0 X X X
1 1 1 1 X X X
I’ll let you do the logic
Next State Logic
Present State
Output
3
Button Input

## Slide 60: Meally version: My Specifications (Digital Debouncer)
If 4 clock cycles after I see a ‘1’, I see a ‘1’, again then I will assume that the input has switched from 01 and I should output a 1.
Whenever I am in the “found a 1” state and I see a 0, I will switch to the wait state.

## Slide 61: Determine I/O (Digital Debouncer)
Button
Output
clk
Cleaned
Button
Output

## Slide 62: Timing Diagram (Digital Debouncer)
Meally Machine
D Q
CLK
CLK
Input
Output
Combinational
Logic
FF Holding
Present State
Output Logic
Takes Present State and Produces Next State.
Input
Output
CLK

## Slide 63: State Transition Diagram (Digital Debouncer)
Wait/Low
000
Sensed 1
001
Sensed 3
011
0/0
1/0
Sensed 2
010
X/0
Sensed 4
100
X/0
X/0
0/0
1/1

## Slide 64: Output Logic (Digital Debouncer)
Output Logic
Present State
Output
3
In P2 P1 P0 Out
0 0 0 0 0
0 0 0 1 0
0 0 1 0 0
0 0 1 1 0
0 1 0 0 0
0 1 0 1 X
0 1 1 0 X
0 1 1 1 X
1 0 0 0 0
1 0 0 1 0
1 0 1 0 0
1 0 1 1 0
1 1 0 0 1
1 1 0 1 X
1 1 1 0 X
1 1 1 1 X
By examination:
Out=In•P2

## Slide 65: Next State Logic (Digital Debouncer)
I’ll let you do the logic
Next State Logic
Present State
Output
3
Button Input
In P2 P1 P0 NS2 NS1 NS0
0 0 0 0 0 0 0
0 0 0 1 0 1 0
0 0 1 0 0 1 1
0 0 1 1 1 0 0
0 1 0 0 0 0 0
0 1 0 1 X X X
0 1 1 0 X X X
0 1 1 1 X X X
1 0 0 0 0 0 1
1 0 0 1 0 1 0
1 0 1 0 0 1 1
1 0 1 1 1 0 0
1 1 0 0 1 0 0
1 1 0 1 X X X
1 1 1 0 X X X
1 1 1 1 X X X

## Slide 66: Today…
Meally to logic
One-hot encoding

## Slide 67: Class Problem
Pattern Finder
  Build a circuit that takes a bit stream in and gives a single high pulse, one clock cycle long, when the pattern has been found. The pattern is: 0010. No overlapping allowed. For example, 00100010 counts as two sequences but 0010010 does not count as two patterns.

## Slide 68: Terms
FSM: A sequential circuit with a finite number of states…
Sequential circuit/logic: A circuit that does things in a specific order
Register: A group of flip-flops