## Slide 1: Lecture 1: Course overview
CIS 240: MICROCOMPUTER ARCHITECTURE & PROGRAMMING
1/22/2025
Due by class: Questionnaire on Canvas
Due by class: Read syllabus

## Slide 2: Me: I’m Tina
My specialties:
  Integrated circuits
  Medical technology
  Digital systems

## Slide 3: You
If you don’t see why we’re doing something, or where it’s useful, ASK!
If debugging hits a wall, email me! (Maybe 30 minutes if not making progress)
I can meet for office hours at almost any time. If scheduled OH don’t work for you, please tell me! And we can find a better time for you.
I prefer you turning something in over me just taking off points. If you can’t get an assignment in on-time, tell me and we’ll work something out.

## Slide 4: Syllabus questions?

## Slide 5: Questionnaire stuff

## Slide 6: Homework
11:59pm
Not Monday
Monday | Tuesday | Wednesday | Thursday | Friday | Saturday | Sunday
4 |  |  |  | 3 |  | 9

## Slide 7: Office hours: In-person
 | Monday | Tuesday | Wednesday | Thursday | Friday | Sat | Sun
10am | 8 |  | 7 |  |  |  | 
11am |  |  |  |  | 1 |  | 
Noon |  | 1 |  | 1 | 1 |  | 
1:20pm | 5 |  | 6 |  |  |  | 
2pm | 1 |  |  |  |  |  | 
3pm |  |  |  |  |  |  | 
4pm |  |  |  |  |  |  | 
5pm |  |  |  |  |  |  | 
This day | 1 | 5 | 1 | 5 | 7 |  | 
TuTh after 2pm
TuTh 10am
Mornings
After 6pm
4-6pm, MW
Not TuTh12:30-2
Virtual 8-9pm

## Slide 8: Textbook
Bait and switch

## Slide 9: Interests
Security (memory unsafe. Memory safe languages include Rust, Go, C#, Java, Swift, Python, and JavaScript.)
Games
Not interested much in this class. Let me program.
Hands on work
Bit manipulation
Memory (Stack, etc.)
Concurrency (Threads, locks…)
Mojo programming language

## Slide 10
Canvas

## Slide 11: Today
Lecture:
  Course overview  “Let’s build a computer”
    Goal: Make sure you know what we’re talking about when we talk about “computer architecture”.
  Numbers
Lab: Numbers practice (Homework will also be number practice)

## Slide 12: Computer hardware…
https://www.pcmag.com/how-to/how-to-build-a-pc-the-ultimate-beginners-guide

## Slide 13: What kind of computer?

## Slide 14: Things to buy
Case
Motherboard
Processor (CPU)
Cooling
Memory
Storage drives
Power supply
(Graphics card)
(WiFi card if not built-in to motherboard or using dongle)
Display, keyboard, mouse, speakers, …

## Slide 15: PC case:
For example: CORSAIR: https://www.corsair.com/us/en/s/pc-case-comparison?_gl=1*wswpfc*_up*MQ..*_gs*MQ..&gclid=Cj0KCQjw_qexBhCoARIsAFgBleuw1ddEZJJSBm01tV0UGNcbBQnWOBRHBeyBprO3DspIjRPc2fQ4OeEaAj_wEALw_wcB
Size?
What motherboard format do you want to use?
  ATX – Largest board. Lotsa slots for adding memory, video card, etc.
  Micro-ATX – smaller. Less slots.
  Mini-ITX – Maybe just a single slot
Color, material…

## Slide 16: Motherboard & CPU: What all future decisions depend on
Motherboard
  newegg: https://www.newegg.com/Motherboards/Category/ID-20
  (1) You need a motherboard that works with the CPU you choose; (Find CPU socket type: AM5, LGA1700…)
  (2) the board should be the right size and shape ("form factor") for your case; and
  (3) it should have the external ports and internal expansion slots you need for what you plan to install.
CPU
  Digikey.com search for CPU  Microprocessors

## Slide 17: Cooling the system:
https://www.youtube.com/watch?v=UoXRHexGIok
https://www.youtube.com/watch?v=7uBNCN6v_gk 0:44
https://www.corsair.com/us/en/s/cpu-coolers-comparison
Cooling
  Fans,
  Heat sinks
  Liquid cooling

## Slide 18: Memory: RAM & Hard drive
https://www.corsair.com/us/en/s/corsair-memory
RAM: DDR4 or DDR5 memory
Hard drive: “the smart default pick with new motherboards is a solid-state boot drive in the M.2 format supporting PCI Express data transfers”.  These days, SSD

## Slide 19: Power supply
https://www.corsair.com/us/en/s/psu-family
ATX power supply or for smaller cases SFX.
Fully wired power supply or modular power supply.

## Slide 20: CPU:
Notes: https://www.istockphoto.com/photo/printed-circuit-board-computer-foundation-cpu-gm2039814500-562597371?utm_campaign=srp_photos_top&utm_content=https%3A%2F%2Funsplash.com%2Fs%2Fphotos%2Fcpu&utm_medium=affiliate&utm_source=unsplash&utm_term=cpu%3A%3A%3A
https://discover.hubpages.com/technology/the-motherboard-components
https://www.alamy.com/stock-photo-pc-computer-open-atx-case-with-motherboard-and-other-hardware-installed-51750805.html?imageid=9874C638-4D68-4A0B-B081-8801F5272BD5&p=81180&pn=1&searchId=ca862c2d60fd8a0b49416e602e3f2185&searchtype=0
https://www.learncomputerscienceonline.com/central-processing-unit/
https://superuser.com/questions/1058555/is-it-possible-to-get-an-internal-usb-port-into-my-notebook

## Slide 22: Course map
Signals between components:
Data
Numbers ①
Compilers ③
Memory ⑤
Addressing schemes
Digital circuits
Gates
Boolean logic
Truth tables
K-Maps ②
Languages/Instructions Hardware
Assembly
Machine language
Architecture Hardware ④
Memory mapped I/O
From Assembly
From C ⑥
Notes: AGP (Accelerated Graphics Port) for graphics cards. Not on most new boards.
IDE (Integrated Drive Electronics), also known as PATA (Parallel ATA), was a standard interface for connecting storage devices like hard drives and optical drives to a motherboard before being replaced by SATA (Serial ATA).
SATA (Serial Advanced Technology Attachment) is a computer interface used for connecting storage devices like hard drives and solid-state drives (SSDs) to a motherboard. Still widely used in desktop and laptop computers. Gradually being supplemented by faster interfaces like M.2 NVMe for SSDs.
PCI (Peripheral Component Interconnect) is a standard computer bus interface for connecting various hardware components to a motherboard. Replaced older bus standards like ISA (Industry Standard Architecture). Gradually superseded by PCI-X and then PCIe (PCI Express).
The North Bridge (also called the Memory Controller Hub or MCH) is a critical component on a motherboard that acts as a high-speed connection hub for the most important system components. Connects the CPU to high-speed components. Manages communications between the processor, RAM, and graphics card.
The South Bridge (also called the I/O Controller Hub or ICH) is a motherboard component that manages slower-speed input/output (I/O) functions and peripheral connections. Handles communication for less critical system components. Connects to various slower-speed interfaces and ports.

## Slide 23: Representing Numbers & Data

## Slide 24: Internal digital representation of NUMBERS
A wire can be 0V or 5V, OFF or ON, LOW or HIGH. These respectively are represented as LOGIC ‘0’ (zero or FALSE) and ‘1’ (one or TRUE).
Each wire or memory cell represents a bit:
  A bit (BInary digiT) is one of these values
REMEMBER: Computers stores all values as 1s and 0s!
  Pictures
  Numbers
  Instructions
  Characters / words
  Data

## Slide 25: Decimal = Base-10
Let’s say you have a number base-10: 298.460
Maximum digit value = Base – 1 = 10 – 1 = 9
Shorthand 298.460  298.46010
104 | 103 | 102 | 101 | 100 | . | 10-1 | 10-2 | 10-3
0 | 0 | 2 | 9 | 8 | . | 4 | 6 | 0
0x104 | 0x103 | 2x102 | 9x101 | 8x100 | . | 4x10-1 | 6x10-2 | 0x10-3
0x104+0x103+2x102+9x101+8x100+4x10-1+6x10-2+0x10-3
Notes: Implicit zeroes

## Slide 26: “Bits” Base-2 (Positive Binary)
Let’s say you have a number base-2: 00110.1102
Maximum digit value = Base – 1 = 2 – 1 = 1
00110.1102 In Base-10:
  =0+0+22+21+0+2-1+2-2+0
  =0+0+4 +2+0+1/2+1/4+0=6.7510
24 | 23 | 22 | 21 | 20 | . | 2-1 | 2-2 | 2-3
0 | 0 | 1 | 1 | 0 | . | 1 | 1 | 0
0x24 | 0x23 | 1x22 | 1x21 | 0x20 | . | 1x2-1 | 1x2-2 | 0x2-3
OFF | OFF | ON | ON | OFF |  | ON | ON | OFF
0x24 +0x23 +1x22 +1x21 +0x20 +1x2-1 +1x2-2 +0x2-3

## Slide 27: Example: Translate 652.62510 to binary (1) (Left of decimal point done on this slide)
  Powers of 2 for positive powers:
  Take integer part: 652
    Find largest power of 2 and subtract:
    652-512=140 (1x29)
    Find largest power of 2 and subtract:
    140-128=12 (1x27)
    Find largest power of 2 and subtract:
    12-8=4 (1x23)
    Find largest power of 2 and subtract:
    4-4=0 (1x22)
210 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
1024 | 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
210 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 28: Example: Translate 652.62510 to binary (2) (Right of decimal point done on this slide)
  Powers of 2 for positive powers:
  Take decimal part: 0.652
    Find largest power of 2 and subtract:
    0.625-0.5=0.125 (1x2-1)
    Find largest power of 2 and subtract:
    0.125-0.125=0 (1x2-3)
    Final value of 652.62510 is:
2-1 | 2-2 | 2-3 | 2-4 | 2-5
0.5 | 0.25 | 0.125 | 0.0625 | 0.03125
2-1 | 2-2 | 2-3 | 2-4 | 2-5
1 | 0 | 1 | 0 | 0
210 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | . | 2-1 | 2-2 | 2-3 | 2-4 | 2-5
0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | . | 1 | 0 | 1 | 0 | 0
Previous slide
This slide

## Slide 29: Example: Translate 652.62510 to binary (3)
Translate 652.62510 to binary
652.62510 = 01010001100.101002
To represent this number in a digital system you need 16 bits, 16 wires, 16 memory cells or 16 somethings…
210 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | . | 2-1 | 2-2 | 2-3 | 2-4 | 2-5
0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | . | 1 | 0 | 1 | 0 | 0

## Slide 30: Class problems 1
Convert 43.12510 to binary
Convert 13.187510 to binary
Convert 444.4410 to binary (limited to 3 numbers to the right of the binary point)

## Slide 31: Translate 01101.0102 to base-10
01101.0102 =
24 | 23 | 22 | 21 | 20 | . | 2-1 | 2-2 | 2-3
0 | 1 | 1 | 0 | 1 | . | 0 | 1 | 0
0x24+1x23+1x22+0x21+1x20+0x2-1+1x2-2+0x2-3 =
0 + 8 + 4 + 0 + 1 + 0 + 0.25 + 0 =13.2510

## Slide 32: Class problem 2
Convert 001011.1012 to decimal
Convert 101.012 to decimal

## Slide 33: Representations: Hexidecimal (base-16)
Binary: 01011101101010101.00111101
  All ones and zeroes
  Not human friendly
Hexadecimal
  Group 4-bits together from decimal point
  4-bits can equal more than 9.
  00001011101101010101.00111101
  0 B B 5 5 . 3 D = 0xBB55.3D
Decimal | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Base-2 | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111
Hex | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
The average person can hold between three and seven items in their short-term memory, also known as working memory. This limit is known as the "magical number seven"

## Slide 34: Representations: Octal (Base-8) (Included for completeness but we won’t use)
Binary: 01011101101010101.00111101
  All ones and zeroes
  Not human friendly
Octal
  Group 3-bits together from decimal point
  01011101101010101.00111101
  1 3 5 5 2 5 . 1 7 2 = 135525.1728
0 0

## Slide 35: Class problems 3
What is the hexidecimal representation of 10010101101010101.10101012?
625.62610 in hex
What’s missing?

## Slide 36: Representing negative numbers (1)
Five ways to represent negative numbers (Four numerical ways):
  Sign-magnitude
    Easy for humans but not so good for math
  1’s complement
    Better for math but wasteful
  2’s complement  The main one we’ll be looking at
    Usually used. Computers like it, not wasteful.
  BCD (Binary-coded decimal)
    Humans like it. Computers… Not so much. Math hard.
  ASCII, JIS X 0208, EUC (Unix), Unicode, etc.
    Text characters

## Slide 37: WORD: Wikipedia
In computing, word is a term for the natural unit of data used by a particular computer design. A word is simply a fixed-sized group of bits that are handled together by the system. The number of bits in a word (the word size or word length) is an important characteristic of a computer architecture.

## Slide 38: 2’s complement in picture form

## Slide 39: Sign-magnitude Representation (1) (Included for completeness but we won’t use)
Let’s pick a number: 2710 = 000110112 = 0x1B
Sign-magnitude says the top bit, the most significant bit (MSB*), the leftmost bit is a sign bit
If the sign bit is “1”, then the number is negative
If the sign bit is “0”, then the number is positive
So….
  000110112 = 2710
  AND
  100110112 = -̶2710
*LSB is the least significant bit and the bit farthest to the right.
Notes: 8-bit number. Can be any number of bits.

## Slide 40: Sign-magnitude Representation (2) (Included for completeness but we won’t use)
A closer look at S/M representation
Question: What is zero?
  000000002 = 010
  AND
  100000002 = -̶010
Two zeroes… That’s a waste of a value.
Later we’ll see that S/M is hardest to use in addition and multiplication of binary numbers.
Number range from: -127 to 127

## Slide 41: One’s complement Representation (1) (Included for completeness but we won’t use)
Let’s pick a number: 2710 = 000110112 = 0x1B
One’s complement says the negative value is just the “complement”. All 1s are changed to zero and all zeroes are changed to ones.
So….
  000110112 = 2710
  AND
  111001002 = -̶2710

## Slide 42: One’s complement Representation (2) (Included for completeness but we won’t use)
Question: What is zero?
  000000002 = 010
  AND
  111111112 = -̶010
Two zeroes… That’s also a waste of a value.
Later we’ll see that 1’s comp is still a little complicated to use in addition and multiplication of binary numbers but quite a bit easier than SM.

## Slide 43: One’s complement Representation (3) (Included for completeness but we won’t use)
What about the number 25510?
  111111112 = 25510
  Invert everything and… 000000002 = 010
  Oops…
It turns out that 1’s comp only works for values between: −(2N−1−1) to (2N−1−1) where N is the number of bits. (Same as S/M)
Here N=8 so values range from –(27-1) to 27-1 or -127 to 127
A closer look will tell you that the MSB tells you if a 1’s comp number is positive or negative

## Slide 44: Two’s complement Representation (1) THIS IS THE MOST IMPORTANT REPRESENTATION
Positive numbers are the same for positive binary and for positive 2’s complement numbers.
Let’s pick a number: 2710 = 000110112 = 0x1B
Two’s complement says the negative value is just the “complement plus 1”. All 1s are changed to zero and all zeroes are changed to ones then 1 is added.
So….
  000110112 = 2710
  AND
  111001002 + 1 = 111001012 = -̶2710

## Slide 45: Class problems 4
Fill in the following table
  All answers in 8-bits except base-10
  If a number can’t be represented, write “X” or “?”
Base-10 | Positive binary | Hexadecimal | 2’s complement
2210 |  |  | 
 | 000100012 |  | 
 |  | 0x81 | 
 |  |  | 000100012
 |  |  | 111110012